## Slide 1: IT Basics ASM - 2
Răzvan Daniel ZOTA
Faculty of Cybernetics, Statistics and Economic Informatics
zota@ase.ro
https://zota.ase.ro/itb

## Slide 2: Contents
Jump & program control instructions

## Slide 3: Conditional jumps
Logic and arithmetic instructions – are setting the flags
The flags are offering information about the previous instructions
Using flags we may transfer (using a conditional jump) the program execution to another instruction inside the program
if the condition was true
  Jump to the specified location
  Instruction Pointer (IP) modifies continuously (to point to the next instruction to be executed)
if the condition was false
  Program is continuing its execution with the next instruction
  IP is incremented as usual

## Slide 4: Conditional jumps(cont.)
The conditional jumps are testing: sign (S), zero (Z), carry (C), parity (P) and overflow (O)
Obs.:
  Val. FFh is greater than 00h for unsigned numbers
  Val. FFh (-1) is less than 00h for signed numbers
  Comparison: unsigned ffh greater than 00h but
  signed ffh less than 00h
Notes: 1 = 00000001
-1 = 11111111
100000000-
1
--------------
11111111 =2^7+2^6+…..

## Slide 5: Numerical comparisons
CMP X,Y(compare) compares two values X and Y
  Like a subtraction that modifies only the flags
  Used to check the contents of a register or a memory location with another value
  Usually it is used with a conditional jump
  CMP AL, 10h ;compares AL with10h (AL doesn’t change)
  JAE SUPER ;if 10h >= then jump to label SUPER
SUB X,Y(subtraction) computes the difference X - Y
  Saves the result in X and sets the flags
Notes: Jump if Above or Equal

## Slide 6: Flags’ settings
CMP Op1, Op2
Unsigned operands Signed operands
Z: eq/not-eq Z: eq/not-eq
C: Op1 < Op2 (C=1) C: no meaning
Op1 >= Op2 (C=0)
S: no meaning S and O together
O: no meaning If ((S=0) and (O=1)) or ((S=1) and (O=0)) then Op1 < Op2
If ((S=0) and (O=0)) or ((S=1) and (O=1)) then Op1 >= Op2

## Slide 7: Comparing signed integers
Let ‘s consider: CMP AX,BX
  The Sign bit (S) will be set function of the result for the operation AX-BX (if it has an 1 in the msb of the result)
  The Overflow flag (O) will be set if the result AX-BX represents a number outside the definition range (-32768 to 32767 for 16-bits) represented as an integer.
Instructions JS (jump on sign) and JL (jump less than)
  JS looks at sign bit (S) for the last comparison or subtraction. If S = = 1 then the jump is done.
  JL verifies the last comparison

## Slide 8: Comparing signed integers (cont.)
JL is true if:
S=1, O=0:
  (AX-BX) negative and (AX-BX) did not produce overflow
  Example (8-bits):
(-5) - (2) = (-7)
The result (-7) has the sign bit set
In this case (-5) is less than (2).

## Slide 9: Jump instructions terminology
The terminology used for the jump instructions is the following:
  Above/Below used for unsigned comparison
  Greater/Less used for signed comparison
Names’ significance:
J => Jump
N => Not
A/B G/L => Above/Below Greater/Less
E => Equal

## Slide 10: Jump instructions’ summary
Instruction Description Conditions
JA=JNBE Jump if above C=0 & Z=0
Jump if not below or equal
JBE=JNA Jump if below or equal C=1 | Z=1
JAE=JNB=JNC Jump if above or equal C=0
Jump if not below
Jump if no carry
JB=JNA=JC Jump if below C=1
Jump if carry
JE=JZ Jump if equal Z=1
Jump if Zero
JNE=JNZ Jump if not equal Z=0
Jump if not zero
JS Jump Sign (MSB=1) S=1

## Slide 11: Jump instructions’ summary (cont.)
Instruction Description Conditions
JNS Jump Not Sign (MSB=0) S=0
JO Jump if overflow set O=1
JNO Jump if no overflow O=0
JG=JNLE Jump if greater
Jump if not less or equal S=O & Z=0
JGE=JNL Jump if greater or equal S=O
Jump if not less
JL=JNGE Jump if less
Jump if not greater or equal
JLE=JNG Jump if less or equal
Jump if not greater
JCXZ Jump if register CX=zero CX=0
Notes: CX general register – “counter” register

## Slide 12: The LOOP instruction
LOOP instruction
  A combination of decrementing CX with a conditional jump
  LOOP is decrementing CX (ECX for 32-bit) and if CX  0 it jumps to the specified label
  When CX is 0, the next instruction is executed
Notes: abc:…..
…..
…..
LOOP abc
…..