## Slide 1: Logic Algebra Part one
Combinational logic

## Slide 2: Contents
Binary logic and logic gates
Boolean Algebra
  Properties
  Algebraic calculus
Standard and canonical forms
  Minterms and maxterms (Canonical forms)
  Sum of products and Product of sums (Standard forms)
Karnaugh maps (K-Maps)
  Functions of 2, 3, 4, 5 variables
  Logic functions simplification using Karnaugh maps

## Slide 3: Basic logic operators
AND (  sau • )
OR (  sau + )
NOT ( )
F(x,y) = x•y,  F is 1 if and only if x=y=1
G(x,y) = x+y,  G is 1 if x=1,or y=1
H(x) = x ,  H is 1 if x=0
Binary operators
Unary operator

## Slide 4: Basic logic operators(cont.)
Logic AND is equivalent with the binary multiplication:
  0 • 0 = 0, 0 • 1 = 0,
  1 • 0 = 0, 1 • 1 = 1
Logic OR is equivalent with binary addition, except one operation:
  0 + 0 = 0, 0 + 1 = 1,
  1 + 0 = 1, 1 + 1 = 1 (≠ 102)

## Slide 5: Truth tables
x | y | F=x•y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
2-Inputs AND
x | y | F=x+y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
2-Inputs OR
x | F=x
0 | 1
1 | 0
NOT

## Slide 6: Logic gates
A logic gate is a graphical representation for the components of electronic circuits and are operating with one or more input signals to produce one output signal
2-Inputs AND
2-Inputs OR
NOT (Inverter)
x
x
x
y
y
F
G
H
F = x•y
G = x+y
H = x

## Slide 7: Diagrams – functions of time
x
y
F=x•y
G=x+y
H=x
1
1
1
1
1
0
0
0
0
0
t0
t1
t2
t3
t4
t5
t6
Input signals
Transitions
Gate signals - output

## Slide 8: Logic combinational circuits
One logic circuit whose output is depending of inputs only is a combinational circuit
In case of the circuits with memory the output may depend on inputs and on values stored in memory– secquential circuit
Let be F = x + y • z + x• y
The logic combinational circuit associated to the function is the following:
x
y
z
F

## Slide 9: Logic combinational circuits (cont.)
In order to make an efficient circuit we must minimize its dimension
The truth table for
  F=x + y • z + x •y
  G=x + y • z
The truth tables for F and G are identical, so we have the same function
To implement the logic circuit we will use G because we need less components
x | y | z | F | G
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0

## Slide 10: Logic combinational circuits(cont.)
x
y
z
F
x
y
z
G
Notes: F(p,q,r,s)=qs+q’s’

## Slide 11: Duality
The dual of a logic expression is obtaining by interchanging operations • and + and the values of 1 and 0 in the initial expression, with respect to the initial precedence of the operations
We do not interchange x with x
Dual example:
  Find H(x,y,z), dual for F(x,y,z) = x  y  z + x  y  z
  H = (x + y + z)  (x + y + z)
Dual expression has not always the same truth value with the initial expression
For a boolean equality the dual expression is also valid.

## Slide 12: Duality properties
1. X + 0 = X 2. X • 1 = X (dual for 1)
3. X + 1 = 1 4. X • 0 = 0 (dual for 3)
5. X + X = X 6. X • X = X (dual for 5)
7. X + X = 1 8. X • X = 0 (dual for 7)

## Slide 13: Other properties of the Boolean Algebra
Absorbtion:
x + x • y = x
x • (x + y) = x (dual)
  Demonstration: x + x • y = x • 1 + x • y = x • (1+y) = x • 1 = x
    Q.E.D.
  2 is true because of the duality principle

## Slide 14: Other properties of the boolean algebra
Consensus theorem
xy + xz + yz = xy + xz
(x+y)•(x+z)•(y+z) = (x+y)•(x+z) -- (dual)
Demonstration: xy + xz + yz = xy + xz + (x+x)yz = xy + xz + xyz + xyz = (xy + xyz) + (xz + xzy) = xy + xz Q.E.D.
2 is true due to the duality principle

## Slide 15: Truth tables
They contain all the possible combinations of the function’s variables
Let be the functions:
  F1(x,y,z) true if at least one input is true
  F2(x,y,z) true if exactly two of inputs are true
  F3(x,y,z) true if all three inputs are true.
x | y | z |  | F1 | F2 | F3
0 | 0 | 0 |  | 0 | 0 | 0
0 | 0 | 1 |  | 1 | 0 | 0
0 | 1 | 0 |  | 1 | 0 | 0
0 | 1 | 1 |  | 1 | 1 | 0
1 | 0 | 0 |  | 1 | 0 | 0
1 | 0 | 1 |  | 1 | 1 | 0
1 | 1 | 0 |  | 1 | 1 | 0
1 | 1 | 1 |  | 1 | 0 | 1

## Slide 16: Truth tables
Which are the expressions of the three logic functions?
  F1(x,y,z) = x + y + z
  F3(x,y,z) = x • y • z
  F2(x,y,z) = (x • y • z) + (x • y • z) + (x • y • z) (1)
= (x • y + x • z + y • z)(x • y • z) (2)
Obs. x • y • z = x + y + z
Notes: DCF=sum of products(minterms)
F2=m3+m5+m6
CCF=product of sums(maxterms)
F2=M0*M1*M2*M4*M7

## Slide 17: Truth tables(cont.)
Truth table: unique representation of a boolean function
If two functions have identical truth tables, the functions are equivalent (and vice versa).
The truth tables can be used to demonstrate diverse equalities.

## Slide 18: The logic expressions are not unique
The expressions that may represent a logic function are not unique
Example:
  F(x,y,z) = x • y • z + x •y•z + x•y•z
  G(x,y,z) = x • y • z + y • z
The truth tables for F() and G() are identical.
In conclusion, F()  G()
x | y | z |  | F | G
0 | 0 | 0 |  | 1 | 1
0 | 0 | 1 |  | 0 | 0
0 | 1 | 0 |  | 1 | 1
0 | 1 | 1 |  | 0 | 0
1 | 0 | 0 |  | 0 | 0
1 | 0 | 1 |  | 0 | 0
1 | 1 | 0 |  | 1 | 1
1 | 1 | 1 |  | 0 | 0

## Slide 19: Algebraic calculus
The boolean algebra is an useful instrument to simplify digital circuits.
Simpler  cheaper, smaller, faster.
Example: simplify the following function:
F = xyz + xyz + xz.
Direct calculus:
F = xyz + xyz + xz = xy(z+z) + xz = xy•1 + xz = xy + xz

## Slide 20: Algebraic calculus (cont.)
Example. Demonstrate that: x y z + x y z + x y z = x z + y z
Demonstration: x y z + x y z + x y z = x y z + x y z + x y z + x y z = x z (y + y) + y z (x + x) = x z •1 + y z •1 = x z + y z Q.E.D.

## Slide 21: Complementary functions
A function’s complementary it is obtained from the initial function interchanging the operations • and +, the values 1 and 0 and complementing each variable.
In the truth table we interchange 1 and 0 in the column representing the value of the function.
The function’s complementary is not the same with the dual function!

## Slide 22: Complementing example
Find H(x,y,z), the complementary for: F(x,y,z) = x y z + x y z
H = F = ( x y z + x y z ) = ( x y z ) • ( x y z ) DeMorgan = ( x+y+z ) • ( x+y+z ) DeMorgan
Observation: A function’s complementary can be obtained from the dual by complementing all the literals

## Slide 23: Minterms/maxterms for a function of two boolean variables
2 variable function |  |  | 
x | y | Minterms mi | Maxterms Mi
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 

## Slide 24: Minterms/maxterms for a function of 3 boolean variables
3 variable function |  |  |  | 
x | y | z | Minterms mi | Maxterms Mi
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Notes: Function of 4 variables: x,y,z,w,
12=1100
m12=xyz’w’
M12=x’+y’+z+w
Function of 5 variables: a,b,c,d,e
25=11001
m25=abc’d’e
M25=a’+b’+c+d+e’

## Slide 25: Example
Let have the following truth table:
DCF for f1 is: f1(x,y,z)= m1 + m2 + m4 + m6 = x y z + x y z + x y z + x y z
CCF for f1 is: f1(x,y,z) = M0 • M3 • M5 • M7 = (x+y+z)•(x+y + z )• (x +y+z )•( x + y + z ).
Observation: mj = Mj
x | y | z |  | f1
0 | 0 | 0 |  | 0
0 | 0 | 1 |  | 1
0 | 1 | 0 |  | 1
0 | 1 | 1 |  | 0
1 | 0 | 0 |  | 1
1 | 0 | 1 |  | 0
1 | 1 | 0 |  | 1
1 | 1 | 1 |  | 0

## Slide 26: Shortcuts: ∑ and ∏
f1(x,y,z) = ∑ m(1,2,4,6), where ∑ represents a sum-of-products, and m(1,2,4,6) represents that the minterms of the sum are m1, m2, m4 and m6.
f1(x,y,z) = ∏ M(0,3,5,7), where ∏ represents a product-of-sums, and M(0,3,5,7) represents that the maxterms of the product are M0, M3, M5 and M7.
Because mj = Mj for any j,
∑ m(1,2,4,6) = ∏ M(0,3,5,7) = f1(x,y,z)

## Slide 27: Conversion between the canonical forms
Replace ∑ with ∏ (or vice versa) and replace those terms of range j which have appeared in the initial form with the ones which haven’t appeared.
Example: f1(x,y,z) = x y z + x y z + x y z + x y z = m1 + m2 + m4 + m6 = ∑(1,2,4,6) = ∏(0,3,5,7) = (x + y + z)•(x + y + z )•( x + y + z )•( x + y + z )

## Slide 28: Standard forms
Standard forms – like the canonical forms, except that not all the literals must appear in the product terms (or sum terms).
Examples:
  f1(x,y,z) = x y z + y z + x z standard sum-of-product
  f1(x,y,z) = (x + y + z)•(y + z )•( x + z ) standard product-of-sums

## Slide 29: Sum-of-product conversion from standard to canonical form
Non-canonical terms are transforming by inserting value 1 for each variable x which is missing: ( x + x ) = 1
Duplicate minterms are removed
f1(x,y,z) = x y z + y z + x z = x y z + ( x + x ) y z + x(y+y)z = x y z + x y z + x y z + x y z + x y z = x y z + x y z + x y z + x y z

## Slide 30: Product-of-sums conversion from standard to canonical form
Non-canonical terms are transforming by inserting value 0 for the variables which are missing (for example, xx = 0) and distributivity property is used
The duplicate maxterms are removed
f1(x,y,z) = (x+y+z)•(y + z )•(x + z ) = (x+y+z)•(xx+y+z)•(x+yy+z ) = (x+y+z)•(x+y +z )•(x +y +z )• (x +y+z)•(x +y +z ) = (x+y+z)•(x+y +z )•(x +y +z )•(x +y+z )

## Slide 31: Karnaugh maps
These maps are graphical representations of the boolean functions.
One cell of the diagram is corresponding to a line in the truth table.
Also, a cell of the diagram is corresponding to a minterm or maxterm of the boolean expression
Zones with multiple adjacent cells are corresponding to standard terms

## Slide 32: Karnaugh map for two variables
m3
m2
1
m1
m0
0
1
0
x1
x2
0
1
2
3
Obs. Variables’ order is important- for f(x1,x2), x1 is the line, x2 is the column.
Cell 0 is representing x1 x2 ; Cell 1 is representing x1 x2; etc. If a minterm appears in the function, then we have a value of 1 in the corresponding cell from the table.
m3
m1
1
m2
m0
0
1
0
x2
x1
0
2
1
3
OR

## Slide 33: Karnaugh map for two variables (cont.)
Any two adjacent cells from the table are differing by only one variable, which appears complemented in one cell and non-complemented in the other cell.
Example: m0 (=x1 x2 ) adjacent with m1 (=x1 x2) and with m2 (=x1x2 ) but not with m3 (=x1x2)

## Slide 34: Karnaugh maps - examples
f(x1,x2) = x1 x2 + x1 x2 + x1x2 = m0 + m1 + m2 = x1 + x2
In the Karnaugh diagram the values of 1 are representing minterms m0, m1, m2
Grouping cells with the value of 1 enable simplification
What simpler functions are represented by each group?
  x1 = m0 + m1
  x2 = m0 + m2
Obs. m0 appears in both groups
x1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
x2
0
1
2
3

## Slide 35: DCF using Karnaugh maps
Completing 1 in the Karnaugh diagram for each product term of the function
Grouping the adjacent cells containing 1 in order to get a product with less variables. The groups must contain a number of cells which are power of 2 (2, 4, 8, …etc.).
For K-maps for 3 or more variables we can group the adjacent terms on the margins. We can group together all the corners.
The groupings or not necessarily unique.

## Slide 36: Karnaugh maps for three variables
m6
m7
m5
m4
1
m2
m3
m1
m0
0
10
11
01
00
yz
x
0
1
3
2
4
5
7
6
Obs.: the variables’ order counts - for (x,y,z), yz is the column, x is the line.
Obs.: each cell is adjacent with three other cells (left, right, up, down or with the corresponding other margin)

## Slide 37: Karnaugh maps for three variables (cont.)
Types of groupings resulted by the minimization process for 2, 4 or 8 cells.
minterm
group of 2 terms
group of 4 terms

## Slide 38: Simplification rules
The minterms of the function are inserted in the table then we group together the cells with the value of 1
Example: f(x,y,z) = xz + xyz + yz
Result: f(x,y,z)= x z + y
 | 1 | 1 | 1
 |  | 1 | 1
x
yz
 | 1 | 1 | 1
 |  | 1 | 1

## Slide 39: More examples
f1(x, y, z) = ∑ m(2,3,5,7)
f2(x, y, z) = ∑ m (0,1,2,3,6)
f1(x, y, z) = x y + xz
f2(x, y, z) = x +y z
yz X | 00 | 01 | 11 | 10
0 |  |  | 1 | 1
1 |  | 1 | 1 | 
1 | 1 | 1 | 1
 |  |  | 1
Notes: 2=010
3=011
5=101

## Slide 40: Four variables diagram
The upper cells are adjacent with the lower cells.
The cells from the right are adjacent with the cells from the left.
m10
m11
m9
m8
10
m14
m15
m13
m12
11
m6
m7
m5
m4
01
m2
m3
m1
m0
00
10
11
01
00
WX
YZ

## Slide 41: 4 variables diagram simplification
One cell is representing a minterm of 4 literals.
One rectangle formed from two adjacent squares is representing a product term of 3 literals.
One rectangle formed from 4 cells is representing a product term of 2 literals.
One rectangle formed from 8 cells are representing a product term of one literal.
One rectangle formed with all the 16 cells is representing a logic function of value 1.
More about minimization of Boolean functions you may find here: https://www.geeksforgeeks.org/minimization-of-boolean-functions/?ref=lbp

## Slide 42: Example
Simplify the logic function:
  f (a,b,c,d) = ∑m(0,1,2,4,5,7,8,9,10,12,13).
We are completing with 1 in the K-diagram associated to f( ) and then we are grouping the values of 1.
cd
ab
1
1
1
1
1
1
1
1
1
1
1
f(a,b,c,d) = c + b d + a b d
1
1
1
1
1
1
1
1
1
1
1
00 01 11 10
00
01
11
10
00 01 11 10
00
01
11
10
ab
cd

## Slide 43: Product-of-sums
0
0
0
0
1
1
0
0
0
1
1
1
1
1
1
1
ab
cd
f(a,b,c,d) = ab + ac + a b c d
Dual for f is: (a+b)(a+c )(a +b+c+d )
Complementing all literals in the dual of (f ): f = (a +b)(a +c)(a+b+c+d)
00 01 11 10
00
01
11
10

## Slide 44: Redundant terms
It may exist combinations of values which:
  Will never happen
  It they are happening, the output doesn’t count
The values of the function for such combinations are expressed by redundant terms.
They are written with R (or x)
The redundant terms can be used to simplify the functions

## Slide 45: Example
Simplify the function f(a,b,c,d) which diagram is:
f = a’c’d+ab’+cd’+a’bc’
or
f = a’c’d+ab’+cd’+a’bd’
The 3rd solution?
x
x
1
1
x
x
0
0
1
0
1
1
1
0
1
0
x
x
1
1
x
x
0
0
1
0
1
1
1
0
1
0
0 | 1 | 0 | 1
1 | 1 | 0 | 1
0 | 0 | x | x
1 | 1 | x | x
ab
cd
00
01
11
10
00
01
11
10
00
01
11
10
00
01
11
10
00
01
11
10
00
01
11
10

## Slide 46: Examples
Simplify the function g(a,b,c,d)
g = a’c’+ ab or
g = a’c’+b’d
x | 1 | 0 | 0
1 | x | 0 | x
1 | x | x | 1
0 | x | x | 0
x | 1 | 0 | 0
1 | x | 0 | x
1 | x | x | 1
0 | x | x | 0
x | 1 | 0 | 0
1 | x | 0 | x
1 | x | x | 1
0 | x | x | 0
ab
cd
Notes: https://www.geeksforgeeks.org/minimization-of-boolean-functions/?ref=lbp