## Slide 1: IT Basics The microprocessor and ASM
Prof. Răzvan Daniel Zota, Ph.D.
Bucharest University of Economic Studies
Faculty of Cybernetics, Statistics and Economic Informatics
zota@ase.ro
https://zota.ase.ro/itb

## Slide 2: Contents
Basic microprocessor architecture
Intel microprocessor registers
Instructions – their components and format
Addressing modes (with examples)

## Slide 3
Basic microprocessor architecture
CPU registers
  Special memory locations on the microprocessor chip
  Examples: accumulator, counter, FLAGS register
Arithmetic-Logic Unit (ALU)
  The place where most of the operations are being made inside the CPU
Bus Interface Unit (BIU)
  It controls data and address buses when the main memory is accessed (or data from the cache memory)
Control Unit and instruction set
  The CPU has a fixed instruction set for working with (examples: MOV, CMP, JMP)

## Slide 4
Instruction’s processing
Processing an instruction requires 3 basic steps:
  Fetching the instruction from memory (fetch)
  Instruction’s decoding (decode)
  Instruction’s execution (execute) – implies memory access for the operands and storing the result
Operation mode of an “antique” Intel 8086
Fetch
1
Decode
1
Execute
1
Fetch
2
Decode
2
Execute
2
…...
Busy
Idle
Busy
…...
Busy
Idle
Busy
Microprocessor
Bus

## Slide 5: Instruction’s processing
Fetch
1
Fetch
2
Fetch
5
Fetch
3
Fetch
4
Modern microprocessors may process more instructions simultaneously (pipelining)
Operation of a pipeline microprocessor (from Intel 80486 to our days)
Store
1
Fetch
6
Fetch
7
Read
2
Decode
1
Decode
2
Decode
3
Decode
4
Decode
5
Decode
6
Idle
Idle
Execute
1
Idle
Execute
2
Execute
3
Execute
4
Execute
5
Execute
6
Generate
Address
1
Generate
Address
2
Bus Unit
Instruction Unit
Execution Unit
Address Unit

## Slide 6: X86 Basic System Architecture
Address Bus
Data Bus
(16 bit)
Control Bus
8086
System
A19
A0
D15
D0
RD/WR
Memory
I/O
To memory
and I/O
Address Bus gives a memory address to the system and a I/O address to I/O system equipment
Data Bus transfers the data between the microprocessor, memory and I/O equipment attached
Control Bus is generating control signals derived from a I/O operation

## Slide 7: Data and memory address dimensions
Processor
8088
8086
80286
80386dx
80486
80586/Pentium (Pro)
Intel/AMD 64 bit
Data Bus
8
16
16
32
32
64
64
Address Bus
20
20
24
32
32
32
40
Maximum addressing memory
1,048,576 (1MB)
1,048,576 (1MB)
16,777,21 (16MB)
4,294,976,296 (4GB)
4,294,976,296 (4GB)
4,294,976,296 (4GB)
1,099,511,627,776 (1TB)
http://www.tomshardware.com/reviews/processor-cpu-apu-specifications-upgrade,3566-2.html

## Slide 8: Microprocessor’s registers
Obs:
32 bit registers do not appear for 8086, 8088, 80286
Notes: AX=1234h
AH=12h
AL=34h
CX=5673h
CL=73h
CH=56h

## Slide 9: General purpose registers
Obs:
32 bit registers do not appear for 8086, 8088, 80286
Base Index
32 biţi
AX
AH
AL
EAX
Accumulator
BH
BL
EBX
BX
Data register
16 biţi
CX
CH
CL
ECX
Counter
DH
DL
EDX
DX

## Slide 10: General purpose registers
Base pointer
16 biţi
SP
ESP
Stack pointer
EBP
BP
Destination index
EDI
DI
Source index
ESI
SI
Obs:
32 bit registers do not appear for 8086, 8088, 80286

## Slide 11: General purpose registers
AX (accumulator) The AX register usually contains the result obtained from a arithmetic/logic operation (see also EAX, AH, or AL)
BX (base) The BX register usually contains the base address (offset) of the data in memory (see also EBX, BH, BL)
CX (count) The specialty of the CX register is counting. It plays the counter role for some specific instructions (see LOOP instruction).
DX (data) The DX register has some specific properties correlated with multiplying and dividing, such as:
  It contains the most significant part of the result in case of multiplying two numbers on 16 or 32 bits;
  It contains the most significant part of the divider before the division;
  It contains the I/O port for some I/O instructions

## Slide 12: Pointer and index registers
SP (stack pointer) The least “general”, used to address data in a memory region of LIFO (last-in, first-out) type: the stack. It is modified in the following cases:
  As a result of PUSH and POP instructions;
  A sub-routine CALL or a return (RET) from a sub-routine of a program;
  Some system resources (the keyboard or internal clock) are using the stack when they interrupt the microprocessor.
BP (base pointer) Used to address a data array in the stack (it is referring to SS-stack segment)
SI (source index) – can be used to address indirectly data
DI (destination index) same as SI
IP (instruction pointer) It is always used to point to the next instruction to be execute by the microprocessor

## Slide 13: The stack
Stack segment
BP (EBP) register
SP (ESP) register
The PUSH instruction determines moving the top of the stack to a lower memory address
The POP instruction determines moving the top of the stack to a higher memory address
Base of stack (initial value SP or ESP)
The BP register it is set up to make a reference to the memory address for returning from the procedure
Return Instruction Pointer
Local variables for the called procedure
The parameters of the called procedure
Top of stack
Notes: 16 bit - 2^16=64KB

## Slide 14: Stack example
BX
CX
SP
BX
CX
SP
1000
?
?
1000
998
996
?
?
?
At the beginning:
998
?
9
1000
998
996
?
9
?
After MOV BX, 9 and PUSH BX:
BX
CX
SP
996
10
9
1000
998
996
10
9
?
After MOV CX, 10 and PUSH CX:

## Slide 15: Stack example
BX
CX
SP
998
10
10
1000
998
996
?
9
?
After POP BX:
BX
CX
SP
1000
9
10
1000
998
996
?
?
?
After POP CX:

## Slide 16: FLAGS register
FLAGS register
O
D
I
T
S
Z
A
P
C
O - Overflow Flag
D - Direction Flag
I - Interrupt Flag
T - Trap Flag
S - Sign Flag
Z - Zero Flag
A - Auxiliary Carry Flag
P - Parity Flag
C - Carry Flag
Notes: FLAGS- 16 bit register
EFLAGS – 32 bit register

## Slide 17: FLAGS register
A flag is a bit that identifies the current state of the microprocessor and its operating mode
The flags are being modified after the execution of some arithmetic or logic instructions
Examples:
  C(carry) flag – it identifies the appearance of a binary carry bit in case of an addition or a borrow in case of a subtraction
  O(overflow) flag – it is modified after an arithmetic operation. If it is set (of value 1) it means that the result doesn’t fit the destination operand
  Z(zero) flag – it means that the result of an arithmetic or logic operation is zero
Notes: Flag is set  flag=1
Flag is not set  flag=0
1+1=10
8 bits -2^8-1=255
250-250

## Slide 18: FLAGS register
  S(sign) flag – it shows the result of an arithmetic operation
  D(direction) flag – when it is zero the processing of the elements is being made from the lower to the upper address and vice versa in the other case
  I(interrupt) flag - it controls the possibility to respond to extern events (interrupt calls)
  T(trap, trace) flag - used by the debugger programs, activating or not the possibility to execute the program step by step. If it is set, the CPU interrupts each instruction, leaving the debugger to execute the program step by step
Notes: S=1-> negative
S=0->positive

## Slide 19: FLAGS register
  A(auxiliary carry) flag – it supports BCD operations.
  P(parity) flag – it is set if the result of an operation contains an even number of 1 bits. If the number of 1s is odd, then PF=0.
Notes: PF=1 result contains an even number of bits
00001110

## Slide 20: Segment registers, IP and FLAGS
FLAGS
32 bits
IP
EIP
IP
EFlags
Flags
Extra segment register
CS
Code segment register
DS
16 biţi
Stack segment register
SS
ES
Data segment register
Additional register (80386, 80486+)
FS
Additional register (80386, 80486+)
GS
Notes: 1234:A412->12340+
A412
------------------------

## Slide 21: Segment registers
CS(code) The code register contains the address for the start of the part of memory which contains the code of the program
DS(data) The data register contains the address for the beginning of the region of memory which contains data
ES(extra) Additional segment register
SS(stack) It defines the region of memory used by the stack.
  The stack pointer register contains the address for the top of the stack
  The BP register contains the address for the data inside the stack
FS and GS available beginning with 80386 and 80486 – additional registers used to access memory segments

## Slide 22: Code machine language
The code machine language represents the native binary code which is “understood” by the microprocessor, containing instructions for its operation
From the assembler program the code machine is generated
The code machine instructions for 8086-80486 varies from 1 to 13 octets
  There are over 20.000 variations of machine code
The real mode use 16 bits instructions
  There are used 16 bits offset addresses and 16 bits registers
Notes: 1MB

## Slide 23: Code machine language (cont.)
The protected mode may use instructions on 16 or 32 bits
  The D bit from the descriptor it shows the way 80386/80486 instructions are using the registers and data from memory in the protected mode
  D = 0 means 80386/80486 16 bits instructions
  D = 1 means 80386/80486 32 bits instructions
  The working mode with 32 bits instructions means that both offset addresses and registers are on 32 bits.

## Slide 24: Addressing modes
Using registers – copy a byte or a word from the source register to the destination register
MOV BX, CX
Effective – copy an effective value (byte or word) from a memory location to a destination register
MOV AX, 3456h
Directly – copy a byte or a word from a memory location specified by a register
MOV AL, [1234h] (1234h represents the offset in the data segment)

## Slide 25: Addressing modes(cont.)
Indirect by registers (indexed) – copy a byte or word from a memory location addressed by an index register (DI or SI) or a base register (BP or BX) in a register:
MOV AX, [BX]
Base plus index (relatively to the base indexed) - copy a byte or word from a memory location specified by a base register (BP or BX) plus an index register (DI or SI) in a register:
MOV DX, [BX + DI]

## Slide 26: Addressing modes(cont.)
Register relative - copy a byte or word from a memory location addressed by an index register (DI or SI) or a base register (BP or BX) plus an offset to a register:
MOV AX, [BX + 1000h]
Base relative plus index (base relative indexed) – copy a byte or word from a memory location specified by a base register (BP or BX) plus an index register (DI or SI) plus an offset, into a register:
MOV AX, [BX + SI + 100h]

## Slide 27: Instruction rules
Each instruction can access memory only once:
  MOV var1,var2 is not a valid instruction
  MOV AX,var2 followed by MOV var1,AX is correct.
For instructions with two operands their dimensions must be the same:
  We may compare an 8 number with another 8 bit number
  We may compare an 16 number with another 16 bit number
  CMP AH,AX is not a valid instruction
The destination operand (normally, the left one) must identify a register or a memory location:
  MOV 1234,AX is not valid
The Mode byte identifies what registers will be used by an instruction

## Slide 28: Addressing examples

## Slide 29: Addressing examples(cont.)

## Slide 30: Addressing examples (cont.)

## Slide 31: Instruction components and format
Instruction’s components:
Opcode
Mode
Displacement
Data/
Effective value

## Slide 32: Instruction’s components
The Opcode byte represents the operation code, the direction (D) and dimension (W)
Mode appears only for instructions that are using registers
The Mode byte represents the destination and source for the instructions with two operands
The destination and source are specified by the REG and R/M fields
D
W
OPCODE
Opcode
Mode
Displacement
Data/
Effective value
MOD
REG
R/M

## Slide 33: Opcode
Opcode (1 or 2 bytes) is selecting the operation (addition, subtraction, move, etc.) to be executed by the microprocessor
D
W
OPCODE
D (direction) – identifies the sense of the operation
D = 0 - from REG to R/M D = 1 - from R/M to REG
W – data’s dimension
W = 0 - byte
W = 1 – word or double word

## Slide 34: Mode
Mode byte has 3 components
Mod specifies addressing type for the instruction with or without
offset
In the case when Mod field contains one of the values 00, 01 or 10, the R/M filed is selecting one of the addressing modes, such as:
  MOV AL, [DI] (no displacement)
  MOV AL, [DI + 2] (8 bits displacement)
MOD
REG
R/M
Mod Function
00 No displacement
01 8 bits displacement
10 16 bits displacement
11 R/M is a register

## Slide 35: REG and R/M values
Code W = 0 (Byte) W = 1(Word) W =1 (Double Word)
000 AL AX EAX
001 CL CX ECX
010 DL DX EDX
011 BL BX EBX
100 AH SP ESP
101 CH BP EBP
110 DH SI ESI
111 BH DI EDI

## Slide 36: Example
Let consider the instruction 8BECh on 2 bytes in binary (assume working on 16 bits)
Binary representation: 1000 1011 1110 1100 Results:
OPCODE: 100010 => MOV
D = W 1 => One word is copied in the register specified in the REG field
MOD 11 => R/M identifies the register
REG 101 => BP register
R/M 100 => SP register
In conclusion, the instruction to be executed is: MOV BP, SP

## Slide 37: Example using R/M
In the case when Mod contains one of the values 00, 01 or 10, the R/M field has a new significance
Example:
  1. If Mod = 00 and R/M = 101 the addressing mode is [DI]
  2. If Mod = 01 or 10 and R/M = 101 the addressing mode is [DI + 33h] or [DI + 2222H], where 33h and 2222h are arbitrary values for the offsets
Code Function
000 DS:[BX+SI]
001 DS:[BX+DI]
010 SS:[BP+SI]
011 SS:[BP+DI]
100 DS:[SI]
101 DS:[DI]
110 SS:[BP]
111 DS:[BX]
Base plus
index
Indirect register

## Slide 38: Example
Let have the instruction 8A15h in machine code
Binary representation is: 1000 1010 0001 0101
OPCODE: 100010 => MOV
D 1 => A word is copied to the register specified by the REG field
W 0 => Byte
MOD 00 => Memory without displacement
REG 010 => DL register
R/M 101 => Addressing mode [DI]
In conclusion, the instruction is: MOV DL, [DI]