## Slide 1: Little Endian vs. Big Endian (Intel vs. Motorola)
Notes: OxABCD
MSB=AB
LSB=CD
Ox12345678
MSB=12
LSB=78

## Slide 2: LITTLE ENDIAN vs. BIG ENDIAN
Let consider the following declarations in C:
unsigned char r1[ ]={1,2,3,4,5,6,7,8,9,10,100,101,102,103,255}
unsigned short r2[ ]={1,2,3,4,5,100,65533,65534,65535}
unsigned int r3[ ]={1,2,3,100,255,4096,12500000}
Notes: 2^16=65536 values
map

## Slide 3: MOTOROLA 68030
Address
0AB012
0102
0304
0506
0708
090A
6465
6667
FF00
0AB022
0001
0002
0003
0004
0005
0064
FFFD
FFFE
0AB032
FFFF
0000
0000
0001
0000
0002
0000
0003
0AB042
0000
0064
0000
00FF
0000
1000
00BE
BC20
0AB052
0000
0000
00FF
0000
0000
0000
0000
0000
0AB062
0064
0000
00FF
0000
0000
0000
0000
0000
r1[0]
r2[0]
r3[0]
r3[6]
Notes: 1000

## Slide 4: INTEL Pentium
Address
0012012
0102
0304
0506
0708
090A
6465
6667
FF00
0012022
0100
0200
0300
0400
0500
6400
FDFF
FEFF
0012032
FFFF
0000
0100
0000
0200
0000
0300
0000
0012042
6400
0000
FF00
0000
0010
0000
20BC
BE00
0012052
0000
0000
00FF
0000
0000
0000
0000
0000
0012062
0064
0000
00FF
0000
0000
0000
0000
0000
r3[6]
r3[0]
r1[0]
r2[0]
Notes: 1000

## Slide 5: Representation example on 64 bits
B1
B2
B3
B4
B5
B6
B7
B8
a) Memory representation for Motorola
B8
B7
B6
B5
B4
B3
B2
B1
b) Memory representation for Intel
Notes: MSB – Most Significand Byte (B1) 1234
LSB – Least Significand Byte (B8)

## Slide 6: Memory – storage capacity
Memory width
Memory address width (16, 20, 24, 32, 40 bits)
Memory address on 16 bits => 216 memory locations (64KB of memory)
Memory address on 20 bits => 220 memory locations (1MB of memory)
Memory address on 24 bits => 224 memory locations (16MB of memory)
Memory address on 32 bits => 232 memory locations (4GB of memory)
Memory address on 40 bits => 240 memory locations (1TB of memory)
Memory address
Notes: Registers of a microprocessor